## Slide 1
Module -IV
Air Compressors

## Slide 2: Air compressor
Pneumatics: A system which uses compressed air is called pneumatics.
It deals with the study of behaviour & application of compressed air
A basic pneumatic system consist of a source of compressed air, control valves, pipelines & pipe fittings and pneumatic accessories like filter, regulator and lubricator

## Slide 3: Application of compressed air
For operating pneumatic tools such as drills, screw drivers, hammers, chisels
For pneumatic cranes
For pneumatic brakes of automobiles, railways and presses
For drive of CNC machine tools
For pneumatic conveying of materials
For pneumatic gauging, inspection and low cost automation systems

## Slide 4: Introduction to compressors
An air compressor is a mechanical device that increases the pressure of air by reducing volume.
Air is compressible, the compressor reduces the volume of air and induces pressure in the air
An air compressor converts electrical energy into pressure energy in the form of the air
The compressed air is stored in the air receiver and can be used for cleaning under pressure, generating torque and develop force using actuators

## Slide 5: Classification of air compressor
Air compressors are classified according to method of energy transfer and pressure generation i.e. positive displacement and (non positive displacement) dynamic compressors
Positive displacement compressors work on the principle of increasing the pressure of air by reducing the volume of air in an enclosed chamber
Dynamic compressors works on the principle of imparting the energy by rotating vanes of impeller on air flowing through casing that increases pressure in air

## Slide 6: Reciprocating Air compressor

## Slide 7: Reciprocating Air compressor

## Slide 8
Reciprocating Compressor – Multistage
High Pressure required by Single – Stage :
Requires heavy working parts.
Has to accommodate high pressure ratios.
Increased balancing problems.
High Torque fluctuations.
Requires heavy Flywheel installations.
This demands for MULTI – STAGING…!!

## Slide 9
Reciprocating Compressor – Multistage
Series arrangement of cylinders, in which the compressed air from earlier cylinder becomes the intake air for the next cylinder.
Intercooler :
Compressed air is cooled
between cylinders.
L.P. = Low Pressure
I.P. = Intermediate
Pressure
H.P. = High Pressure
L.P.
Cylinder
I.P.
Cylinder
H.P.
Cylinder
Intercooler
Intercooler
Air Intake
Air Delivery

## Slide 10: Double stage reciprocating air compressor

## Slide 11: Rotary vane compressor

## Slide 12: Centrifugal compressor

## Slide 13: Axial flow compressor